WbMaster

This is type of synchronous master, which means that from pc is send only one command, until is received answer from communication.

All components are:
1. UartRx
  1. out_data[7:0] – Receiving 8 bits in the sequence from input,. And when whole word is completed, send result about 7 bits long to the output.
  2. Rx_done – when transfer is completed, together with that is set signal which indicate transfer complete. This signal is active just for one period.
2. Uart2wb
  1. UART_in_data[7:0] – word from UartRx
  2. UART_rx_done – input signal, indicate new data in the word UART_in_data. Active for one period.
  3. WB_ctr_w[33:0]
    1. control word from WbMaster. Higher two bits on index[33:32], are determined for distinction between commands: W-write, R-read, A-address.
    2. Rest of bits [31:0] are data bits.
  4. WB_o_cyc – when is from UartRx received another word, which indicating some command, than previous WB_ctr_w is send to master. And this signal is active, consequence to he new data to the WbMaster. This signal is hold active for one period.
3. WbMaster
4. WB2UART
5. UartTx

Result from WbMaster is send back, just for read and write commands.
Chars for Uart2wb/WB2UART are recevied/send in MSB order(that means, that data [31:28] are send first, if we disregard control byte).

WB2UART
When this module receive new word about length of 8 words, even if control word contains for example just first byte with some information and rest are all zeros, the Uart2wb module still sends 9 bytes to the UartTx.

Table of input data:
Address - 0x41
Write - 0x57
Read - 0x52

Idea for future – Because MSB is send first, we can check if byte is equal to zero, and skip to next byte. After that if byte isnt equal to zero, rest of bytes will be sent even if are equal to zero.

WbMaster
This module is heard of entire system. Received commands through Uart modules, and returns results back to another Uart modules.
And secondly communicate with slaves via Wishbone communication.

Simulace

In simulation we don’t use modules UartRx and UartTx, because they are to much slow.
Maybe this is nonsense.